## Slide 1: ZigZag-Project: Enabling Fast Architecture-Mapping DSE for Deep Learning Accelerators
Arne Symons, Linyan Mei, Guilherme Paim
Prof. Marian Verhelst
MICAS Labs, ESAT, KU Leuven, Belgium
ISPASS2023 Tutorial

## Slide 2: Tutorial Outline
Introduction (8:30 – 8:50)
Lab 1: Assess HW performance of DNN layer onto accelerator, with fixed temporal mapping (8:50 – 9:30)
Lab 2: Automate temporal mapping optimization (9:30 – 10:00)
Break (10:00 – 10:30)
Lab 3: Understand the HW architecture definition (10:30 – 11:00)
Lab 4: Explore layer-fused mappings on multi-core architectures using Stream (11:00 – 11:45)
Concluding remarks (11:45 – 12:00)

## Slide 3: ZigZag Project
Linyan Mei
Pouya Houshmand
Arne Symons
Project started Dec. 2018
Many contributors
Steven Colleman
Guilherme Paim
Koen Goetschalckx
Prof. Marian Verhelst
Vikram Jain
Victor JUNG (ETHz)
Sebastian Karl (TUM)

## Slide 4
Algorithm
Mapping/
Scheduling
Technology
HW Arch.
Application
A high-level view
ZigZag-project

## Slide 5: DNN Layer
A DNN Conv2D layer:
3D operand (W/I/O) space.
7D nested for-loop MAC operation.
Each Operand has its own (ir)relevant loop dimensions.
r loops contribute to data size.
ir loops contribute to data reuse.
pr loops contribute to both
data size and data reuse.

## Slide 6: DNN Layer
Most ML workloads fit into the regular nested for-loop format.
No data dependency between each for-loop.
Conv2D
MMM

## Slide 7: DNN Accelerator
PE
PE
PE
PE
W – L1
W – L2
Off-chip DRAM
PE
PE
PE
PE
I – L2
O – L2
I – L1
O – L1
PE
PE
PE
PE
PE
PE
PE
PE
PE
…
PE Design
PE Array & Interconnects
Memory Hierarchy
Large Design Degrees of Freedom!
…
I
W
O
…

## Slide 8: Mapping (a.k.a. Dataflow)
PE
PE
PE
PE
W – L1
W – L2
Off-chip DRAM
PE
PE
PE
PE
I – L2
O – L2
I – L1
O – L1
PE
PE
PE
PE
PE
PE
PE
PE
W – Reg
I – Reg
O – Reg
MAC
Temporal Mapping
(Loop tilling, ordering)
Spatial Mapping
(Loop unrolling)
Operation Parallelism
Data Stationarity
Large Design Degrees of Freedom!

## Slide 9: Loop Ordering and Splitting
I
W
O
×
=
C=8
B=3
K=4
C=8
K=4
B=3
for b in [0: 3):
for k in [0: 4):
for c in [0: 8):
O[b][k] = I[b][c] × W[k][c]
for b in [0: 3):
for k in [0: 4):
for c in [0: 8):
O[b][k] = I[b][c] × W[k][c]
for b in [0: 3):
for c in [0: 8):
for k in [0: 4):
O[b][k] = I[b][c] × W[k][c]
for k in [0: 4):
for c in [0: 8):
for b in [0: 3):
O[b][k] = I[b][c] × W[k][c]
for k2 in [0: 2):
for c in [0: 8):
for b in [0: 3):
for k1 in [0: 2):
O[b][2k2+k1] = I[b][c] × W[2k2+k1][c]

## Slide 10: Co-Exploration
Algorithm
Mapping
Hardware
Technology and Others
Technology: 65nm/40nm/28nm/…,
NVM, CIM, 3D IC, etc.
Others: Sparsity, various precisions, cross-layer execution, etc.
HUGE design space at each level & at combined levels.
Regular workload & Deterministic processing flow & Well-defined HW components.

## Slide 11: Getting Started: Codespaces
Select ispass2023-tutorial
Create codespace
https://github.com/ZigZag-Project/zigzag

## Slide 12: Getting Started: Manual Clone
$ git clone git@github.com:ZigZag-Project/zigzag.git
$ cd zigzag
$ conda create --name my-zigzag-env python=3.10
$ conda activate my-zigzag-env
$ pip install –r requirements.txt
$ git checkout ispass2023-tutorial
$ code .
https://github.com/ZigZag-Project/zigzag

## Slide 13: Lab 1: ZigZag Cost Model
Open lab1/main.py
Expects three arguments:
  accelerator
  model
  mapping
Extracts names from the given arguments and sets inputs
Defines the sequence of stages to be executed
Runs the sequence of stages with inputs
Plots the returned CostModelEvaluation (CME)

## Slide 14: Lab 1: ZigZag Cost Model
Model (workload)
First layer of ResNet18 (ONNX format)

## Slide 15: Lab 1: ZigZag Cost Model
Accelerator
TPU-like architecture
Global Buffer
(I1/O)
O
O
O
O
DRAM
(I1/I2/O)
.....
I2
MAC
I2
MAC
I2
MAC
I2
MAC
.....
I2
I2
MAC
MAC
I2
MAC
I2
MAC
I2
MAC
I2
MAC
I2
MAC
I2
MAC
I2
MAC
I2
MAC
I2
MAC
D1 : 32
D2 : 32

## Slide 16: Lab 1: ZigZag Cost Model
Mapping
Defines mapping of layers onto accelerator

## Slide 17: Lab 1: ZigZag Cost Model
Global Buffer
(I1/O)
Unroll C
O
O
O
O
DRAM
(I1/I2/O)
.....
I2
MAC
I2
MAC
I2
MAC
I2
MAC
.....
I2
I2
MAC
MAC
I2
MAC
I2
MAC
I2
MAC
I2
MAC
I2
MAC
I2
MAC
I2
MAC
I2
MAC
I2
MAC
Unroll K
D1 : 32
D2 : 32

## Slide 18: Lab 1: ZigZag Cost Model
Mapping
Defines mapping of layers onto accelerator

## Slide 19: Lab 1: ZigZag Cost Model
Global Buffer
(I/O)
Unroll C
O
O
O
O
DRAM
(I/W/O)
.....
W
MAC
W
MAC
W
MAC
W
MAC
.....
W
W
MAC
MAC
W
MAC
W
MAC
W
MAC
W
MAC
W
MAC
W
MAC
W
MAC
W
MAC
W
MAC
Unroll K
D1 : 32
D2 : 32
I1  I I2  W O  O

## Slide 20: Lab 1: ZigZag Cost Model
  First experiment:
model = “lab1/resnet18_first_layer.onnx”
accelerator = “zigzag.inputs.examples.hardware.TPU_like”
mapping = “mapping”
Run lab1/main.py

## Slide 21: Lab 1: ZigZag Cost Model
  Second experiment:
Modify lab1/mapping.py:
  Change temporal loop ordering
  Run lab1/main.py

## Slide 22: Lab 2: Automating temporal mapping
Copy lab1/main.py  lab2/main.py
Replace TemporalOrderingConversionStage  LomaStage
Change dump_filename_pattern
Change plotting save_path
Copy lab1/mapping.py  lab2/mapping.py
Remove temporal_ordering

## Slide 23: Lab 2: Automating temporal mapping
  First experiment:
model = “lab2/resnet18_first_layer.onnx”
accelerator = “zigzag.inputs.examples.hardware.TPU_like”
mapping = “mapping”
Run lab2/main.py

## Slide 24: Lab 2: User-defined workload
Copy lab2/main.py  lab2/main_user_defined.py
Replace ONNXModelParserStage WorkloadParserStage
Change dump_filename_pattern
Change plotting save_path

## Slide 25: Lab 2: User-defined workload
  Second experiment:
model = “resnet18_first_layer”
accelerator = “zigzag.inputs.examples.hardware.TPU_like”
mapping = “mapping”
Run lab2/main_user_defined.py

## Slide 26: Intermezzo: API
ZigZag is also distributed on PyPI
API call for common use-case

## Slide 27: Break
Lab 3 & 4 after the break
Start at 10.30 AM

## Slide 28: Lab 3: Architectural impact
Open lab3/inputs/hardware/c_k.py
  Definition of multiplier array
  Definition of memory hierarchy
  Definition of core

## Slide 29: Lab 3: c_k.py
memory_instances
dram
rf_1B
rf_4B
l1_w
l2_w
l1_io
l2_io

## Slide 30: Lab 3: c_k.py
.....
MAC
MAC
MAC
MAC
.....
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
D1 : 32
D2 : 32
multiplier_array

## Slide 31: Lab 3: c_k.py
.....
MAC
MAC
MAC
MAC
.....
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
I2
D1 : 32
D2 : 32
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
multiplier_array
rf_1B

## Slide 32: Lab 3: c_k.py
...
MAC
MAC
MAC
MAC
.....
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
I2
D1 : 32
D2 : 32
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I1
I1
I1
I1
multiplier_array
rf_1B
rf_1B

## Slide 33: Lab 3: c_k.py
...
MAC
MAC
MAC
MAC
.....
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
I2
D1 : 32
D2 : 32
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I1
I1
I1
I1
O
O
O
O
multiplier_array
rf_1B
rf_1B
rf_4B

## Slide 34: Lab 3: c_k.py
...
MAC
MAC
MAC
MAC
.....
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I1
I1
I1
I1
O
O
O
O
I2
multiplier_array
rf_1B
rf_1B
rf_4B
l1_w

## Slide 35: Lab 3: c_k.py
...
MAC
MAC
MAC
MAC
.....
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I1
I1
I1
I1
O
O
O
O
I2
I1/O
multiplier_array
rf_1B
rf_1B
rf_4B
l1_w
l1_io

## Slide 36: Lab 3: c_k.py
...
MAC
MAC
MAC
MAC
.....
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I1
I1
I1
I1
O
O
O
O
I2
I1/O
I2
multiplier_array
rf_1B
rf_1B
rf_4B
l1_w
l1_io
l2_w

## Slide 37: Lab 3: c_k.py
...
MAC
MAC
MAC
MAC
.....
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I1
I1
I1
I1
O
O
O
O
I2
I1/O
I2
I1/O
multiplier_array
rf_1B
rf_1B
rf_4B
l1_w
l1_io
l2_w
l2_io

## Slide 38: Lab 3: c_k.py
...
MAC
MAC
MAC
MAC
.....
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
MAC
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I2
I1
I1
I1
I1
O
O
O
O
I2
I1/O
I2
I1/O
I1/
I2/
O
multiplier_array
rf_1B
rf_1B
rf_4B
l1_w
l1_io
l2_w
l2_io
dram

## Slide 39: Lab 3: Architectural impact
Open lab3/inputs/hardware/c_k.py
  Definition of multiplier array
  Definition of memory hierarchy
  Definition of core
Open lab3/inputs/mapping/…
  Definition of spatial mappings

## Slide 40: Lab 3: Architectural impact
Open lab3/inputs/hardware/c_k.py
  Definition of multiplier array
  Definition of memory hierarchy
  Definition of core
Open lab3/inputs/mapping/…
  Definition of spatial mappings
Open lab3/main.py
  Uses API call for every core architecture mapping
  Uses API call for architecture comparison plot

## Slide 41: Lab 3: Architectural impact
  First experiment:
Run lab3/main.py

## Slide 42: Conclusion: ZigZag
Hardware accelerator model based on array of multipliers and attached memory hierarchy
Hardware performance estimation of DNN layer through analytical cost model
Optimization of layer mapping through different stages
Enables co-exploration of accelerator & mapping

## Slide 43: From ZigZag to Stream
Frameworks | Workload | Hardware | Mapping
ZigZag | A NN layer | Single-core accelerator | Single-layer mapping
Stream | One/more NN(s) | Multi-core accelerator | Fine-grained layer-fused mapping
Focus on Stream for the rest of the session

## Slide 44
Traditional DNN Acceleration
An example workload
Layer 4
Layer 1
Layer 0
Layer 2
Layer 3
L4
L0
L1
L2
L3
Core 0
Timeline
An example accelerator
Acceleration timeline
DRAM

## Slide 45
Multi-core DNN Acceleration
An example workload
Layer 4
Layer 1
Layer 0
Layer 2
Layer 3
A multi-core accelerator
Acceleration timeline
C0
DRAM
C1
C2
C3
Timeline
C0
C1
C2
C3
0
2
3
1
4

## Slide 46
Layer-fused processing
Tiled for layer-fused processing
A multi-core accelerator
Acceleration timeline
C0
DRAM
C1
C2
C3
Timeline
L4
L4
L1
L1
L0
L0
L2
L2
L3
L3
C0
C1
C2
C3
0
1
2
3
4
0
1
2
3
4

## Slide 47
Stream
C0
DRAM
C1
C2
C3
 | Single-core | Multi-core
Layer-by-layer |  | 
Layer-fused |  | 
0
1
2
3
4
0
1
2
3
4
Core 0
Timeline
An example workload
Hardware
Schedule
Schedule the workload to hardware accelerators
L4
L0
L1
L2
L3
Core 0
(1)
(2)
L4
L4
L1
L1
L0
L0
L2
L2
L3
L3
Tiled for layer-fused scheduling
Layer 4
Layer 1
Layer 0
Layer 2
Layer 3
C0
C1
C2
C3
0
2
3
1
4
C0
C1
C2
C3
0
1
2
3
4
0
1
2
3
4
(3)
(4)
SotA frameworks
DeFiNES, TVM-Cascade, Stream
SotA frameworks
ZigZag, Timeloop, …, Stream
Kwon et al. 2021, Stream
Stream
DRAM
Memory
Compute
Core 0

## Slide 48
What can Stream do?
Model single-core architecture (identical to ZigZag)

## Slide 49
What can Stream do?
C0
DRAM
C1
C2
C3
DRAM Rd. Bus
DRAM Wr. Bus
C0
DRAM
C1
C2
C3
DRAM Bus
C0
DRAM
C1
C2
C3
DRAM Bus
C0
DRAM
C1
C2
C3
DRAM Bus
Comm. Bus
Model single-core architecture (identical to ZigZag)
Model different multi-core topologies

## Slide 50
What can Stream do?
Model single-core architecture (identical to ZigZag)
Model different multi-core topologies
Model different scheduling granularities

## Slide 51
Latency-optimized schedule
Memory-optimized schedule
What can Stream do?
Model single-core architecture (identical to ZigZag)
Model different multi-core topologies
Model different scheduling granularities
Model different scheduling heuristics

## Slide 52: Stream Overview
ZigZag

## Slide 53: Getting Started: Codespaces
Select ispass2023-tutorial
Create codespace
https://github.com/ZigZag-Project/stream

## Slide 54: Getting Started: Manual Clone
$ git clone git@github.com:ZigZag-Project/stream.git
$ cd stream
$ conda create --name my-stream-env python=3.10
$ conda activate my-zigzag-env
$ pip install –r requirements.txt
$ git checkout ispass2023-tutorial
$ code .
https://github.com/ZigZag-Project/stream

## Slide 55: Lab 4: Stream
Open lab4/main_fixed.py
Defines inputs directly in file instead of arguments
Extracts (from input names) and defines variables
Sets up the sequence of stages
Runs the stages
Plots the results

## Slide 56: Lab 4: Stream
Workload
Open lab4/inputs/workload/duplicated_resnet18_layer_fixed.py
First layer of ResNet18 duplicated 4 times
Dependencies between the layers (operand_source)
operator_type overloaded for fixed mapping

## Slide 57: Lab 4: Stream
Accelerator
Open lab4/inputs/hardware/heterogeneous_quadcore.py
Imports the “computational cores”
Imports the pooling and simd cores
Imports the offchip core
Creates a 2D mesh of these cores
Defines the multi-core Accelerator object

## Slide 58: Lab 4: Stream
Mapping
Open lab4/inputs/mapping/mapping_fixed.py
Defines for each operator_type the possible layer-core allocations

## Slide 59: Lab 4: Stream
  First experiment:
model = “...duplicated_resnet18_layer_fixed”
accelerator = “…heterogeneous_quadcore”
mapping = “…mapping_fixed”
Run lab4/main_fixed.py

## Slide 60: Lab 4: Stream
  Second experiment:
What happens if we remove the layer dependencies?
Remove the operand_source and modify the constant_operands
Run lab4/main_fixed.py

## Slide 61: Lab 4: Stream
  Third experiment:
Allow genetic algorithm to find best layer-core allocation
model = “...duplicated_resnet18_layer”
  Modified operator_type
mapping = “…mapping”
  Modified for flexible layer-core allocation
Run lab4/main_layer_by_layer.py

## Slide 62
Layer Fusion: Computation Node (CN)
Computation node (CN) granularity impacts scheduling flexibility
and others…
Core utilization
Intra-CN data reuse
Data loading overhead
Control overhead

## Slide 63: Lab 4: Stream
Open lab4/main_layer_fused.py
hint_loops defines the outer-CN loops
  hint_loops = [(“OY”, 2)] means 2 CNs per layer
  hint_loops = [(“OY”, “all”)] means OY CNs per layer

## Slide 64: Lab 4: Stream
  Fourth experiment:
Assess the impact of layer-fused processing
Run lab4/main_layer_fused.py

## Slide 65: Lab 4: Stream
Open lab4/main.py
End-to-end ResNet18 onnx model
Layer-by-layer

## Slide 66: Lab 4: Stream
  Last experiment:
End-to-end ResNet18 example
Run lab4/main.py (layer-by-layer)
If time permits:
  Modify hint_loops with (“OY”, “all”)
  Re-run and analyze differences

## Slide 67: What’s to come?
Automatically infer optimal CN granularity
Integrate inter-core connect energy estimation framework
Automatically search for optimal multi-core architectures
Add optimization constraints (e.g. max latency, area, …)
Code generation for existing accelerators
Automatic hardware generation from hardware templates

## Slide 68: Conclusion
ZigZag enables fast hardware performance estimation for specialized DNN accelerator architectures
Mapping optimizations yield better performance
Co-exploration of architecture with mapping
Stream extends the capabilities to multi-core architectures employing layer-fused scheduling
Unified hardware model for different architecture topologies
Different scheduling granularities through computation node

## Slide 69: Materials of ZigZag-project
Goal: Enabling Fast Architecture-Scheduling/Mapping DSE for Machine Learning Accelerators
Github: https://github.com/ZigZag-Project
  ZigZag
  ZigZag-Demo
  DeFiNES
  Stream
ZigZag documentation: https://zigzag-project.github.io/zigzag/
Stream documentation: Underway (end of May)
ZigZag-related publications:
https://zigzag-project.github.io/zigzag/publications.html